## Slide 1
Quick Guide
How to change screen

## Slide 2
1
How to change screen
Use ‘Change Screen Switch’ object
3 Ways to change screen
Use ‘Change screen by device’
Use Script

## Slide 3
2
‘Change Screen Switch’ has 2 types of Device and Constant
How to change screen
Use ‘Change Screen Switch’ object
①
②
①
If device, the screen will change to the screen if there is a base screen number which equals the device value.
If constant, a screen number must be selected and the switch will change the screen to the specific screen.
②
If fixed, a screen number must be selected and the switch will change the screen to the specific screen.
If previous, a screen will change to the previous screen.
※ If device type is selected, but there is no base screen matching the value of word device, then the switch cannot be touched.

## Slide 4
3
Go to Project Property → Screen Settings
How to change screen
Use ‘Change screen by device’
When ‘Change to screen number’ is checked, you can insert a device.
This device should be WORD type.
If WORD device is selected, the screen will change to the screen if there is a base screen number which equals the device value.
※ If there is no base screen matching the value of word device, then screen will not change.

## Slide 5
4
How to change screen
Use Script
①
②
Go to View → Script Toolbox to get help of using script easily.
Use Script function ‘ChangeBaseScreen ( no. ) ; this script will change the screen to specific screen.
※ There are several ways to use script. Please refer to manual for further information.